## Slide 1
Module 3: Grid Driving
Introduction to the Grid
Learning Objectives
Describe the physical grid layout and how intersections are formed
Explain how cross detection from Module 2 maps to grid intersections
Use the driving toolkit to drive to the first intersection
Reuse existing code on a new surface
Agenda
From circle to grid (10 min)
Review: driving toolkit functions (5 min)
Guided: Drive to first intersection (15 min)
Practice (15 min)

## Slide 2
Hook — From Circle to Grid
Remember Module 2?
You built a driving toolkit that follows lines and detects crosses
Now look at this grid:
Lines running horizontally and vertically
Where they cross = intersection
Each intersection looks just like the cross on the circle!
Question: "Can your Module 2 code work on this grid without changes?"
Answer: Yes! That's the power of code reuse.

## Slide 3
The Grid Layout
A grid is a network of taped lines:
 | Col 0 | Col 1 | Col 2 | Col 3
Row 0 | + | + | + | +
Row 1 | + | + | + | +
Row 2 | + | + | + | +
Row 3 | + | + | + | +
Each "+" is an intersection:
Lines connecting them horizontally and vertically
The robot follows lines between intersections
Cross detection tells the robot it has arrived

## Slide 4
Why the Grid Matters
The grid is a stepping stone:
Module 2: Follow a circle, detect one cross
Module 3 (now): Navigate a GRID of crosses
Module 4: Use COORDINATES on the grid for pathfinding
Grid navigation = line following + cross detection + turns
You already have all three from Module 2!

## Slide 5
Review — Driving Toolkit Functions
Your driving toolkit from Module 2 has three key functions:
# Follow the line until an intersection
track_until_cross()
# Turn right onto perpendicular line
turn_right()
# Turn left onto perpendicular line
turn_left()
These three methods are ALL you need for grid navigation!

## Slide 6
Driving to the First Intersection
Setup: Place robot on a grid line, behind an intersection
Program:
board = Board.get_default_board()
board.wait_for_button()
print("Driving to first intersection...")
track_until_cross()
print("Intersection reached!")
What happens:
Robot follows the line using proportional control
When both sensors detect the cross → stops
Robot is now AT the intersection

## Slide 7
Drive and Turn
After reaching an intersection, you can turn:
board.wait_for_button()
track_until_cross()
print("At intersection!")
turn_right()
print("Turned right - now on perpendicular line!")
track_until_cross()
print("At next intersection!")
The robot:
Follows the line to the first intersection
Turns right onto the crossing line
Follows THAT line to the next intersection

## Slide 8
Code Reuse in Action
Module 2 code → Module 3 application:
Module 2 | Module 3
Follow circle | Follow grid lines
Detect cross on circle | Detect grid intersection
Turn at cross | Turn at intersection
`track_until_cross()` | Same method, same code!
`turn_right()` | Same method, same code!
Key insight: Good code works in new situations without modification.

## Slide 9
Your Turn!
Activity:
Copy your sensor and driving toolkits from Module 2
Write a program that drives to the first intersection and stops
Verify the robot stops at the right place
Add a turn_right() after reaching the intersection
Add another track_until_cross() to drive to the next intersection
Checkpoints:
Does the robot stop at the first intersection?
Does the turn line up with the perpendicular line?
Does the robot reach the second intersection after turning?

## Slide 10
Connection to Next Lesson
What you did today:
Saw how the grid relates to Module 2's cross detection
Drove to the first intersection using the driving toolkit
Added a turn at the intersection
Next lesson (Lesson 2):
Drive PAST an intersection to reach the next one
Learn the "clear the intersection" technique
Use for loops to drive multiple intersections
Challenge: What if you need to go 3 intersections forward? That's next!