## Slide 1
Module 2: Line Tracking
Proportional Control Review
Before we move on, let's make sure we REALLY understand
what proportional control is doing — not just the code, but the idea.

## Slide 2
The Shower Analogy
Proportional control is something you already do every day.
Situation | How you feel | What you do
Water is WAY too cold | Very uncomfortable | Turn knob a LOT toward hot
Water is a little too cold | Slightly uncomfortable | Turn knob a LITTLE toward hot
Water is just right | Comfortable | Do nothing
Water is a little too hot | Slightly uncomfortable | Turn knob a LITTLE toward cold
Water is WAY too hot | Very uncomfortable | Turn knob a LOT toward cold
The key idea: How much you turn the knob depends on how far off the temperature is.
A little off? Small adjustment. Way off? Big adjustment.
That is proportional control. The response is PROPORTIONAL to the error.

## Slide 3
The Same Idea, Applied to the Robot
White surface LINE White surface
A B C D E
(far (a bit (on the (a bit (far
left) left) edge) right) right)
Position | Sensor reads | How far off? | Robot does
A (far left of line) | 0.1 | Very far | Steer HARD toward line
B (a little left) | 0.3 | A little | Steer gently toward line
C (on the edge) | 0.5 | Perfect | Drive straight
D (a little right) | 0.7 | A little | Steer gently away from line
E (far right of line) | 0.9 | Very far | Steer HARD away from line
Same principle as the shower: bigger error = bigger correction

## Slide 4
What is "Error"?
Error = how far am I from where I want to be?
error = setpoint - sensor_reading
0.0 0.2 0.4 0.5 0.6 0.8 1.0
|——white----|---------|---*---|---------|----black------|
setpoint
Sensor reads 0.2: error = 0.5 - 0.2 = +0.3 (steer toward line -->)
Sensor reads 0.5: error = 0.5 - 0.5 = 0.0 (perfect, go straight)
Sensor reads 0.8: error = 0.5 - 0.8 = -0.3 (<-- steer away from line)
• The SIGN (+/-) tells you WHICH DIRECTION to steer
• The SIZE (big/small) tells you HOW MUCH to steer

## Slide 5
What is Kp?
Kp controls how aggressively the robot reacts. Think of Kp as the robot's personality:
Kp value | Personality | Behavior
Low (0.1) | 😴 "Lazy robot" | Barely reacts, drifts off the line
Medium (0.5) | 🙂 "Calm robot" | Smooth, steady corrections
High (2.0) | 😰 "Nervous robot" | Overreacts, zigzags wildly
correction = error * Kp
Same error, different Kp:
error | Kp = 0.1 | Kp = 0.5 | Kp = 2.0
+0.3 | 0.03 (tiny steer) | 0.15 (moderate) | 0.60 (HUGE steer)
-0.3 | -0.03 (tiny steer) | -0.15 (moderate) | -0.60 (HUGE steer)
Kp is a volume knob for the correction.

## Slide 6
What Does This Look Like on the Track?
Kp too low (0.1) — "Lazy robot"
Line: ~~~~~~~~~~~~~~~~~~~~~~~~~~~~
Robot: ~~~~~~~~~~~~~~~
~~~~~~~ (drifts off)
Robot reacts too slowly, drifts off on curves
Kp just right (0.5) — "Calm robot"
Line: ~~~~~~~~~~~~~~~~~~~~~~~~~~~~
Robot: ~~~~~~~~~~~~~~~~~~~~~~~~~~~~ (smooth!)
Robot follows smoothly with small adjustments
Kp too high (2.0) — "Nervous robot"
Line: ~~~~~~~~~~~~~~~~~~~~~~~~~~~~
Robot: ~/\/\/\/\/\/\/\/\/\/\/\/\~ (zigzag!)
Robot overcorrects, oscillates wildly
The goal of tuning: find the Kp where the robot follows smoothly without oscillating.

## Slide 7
The Four Steps — Every Single Loop
The control loop does the same four steps, hundreds of times per second:
+---> 1. READ SENSOR ----> 2. CALCULATE ERROR ---+
| (where am I?) (how far off?) |
| |
+--- 4. SET MOTORS <---- 3. CALC CORRECTION ----+
(adjust steering) (how much to fix?)
Trace it with real numbers:
1. Read sensor: sensor_value = 0.2
2. Calculate error: error = 0.5 - 0.2 = +0.3
3. Calculate correction: correction = 0.3 * 0.5 = 0.15
4. Set motors: arcade(0.3, 0.15)
--> left motor = 0.3 + 0.15 = 0.45
--> right motor = 0.3 - 0.15 = 0.15
--> robot steers right, toward the line
Then it does it again. And again. And again. Hundreds of times per second.

## Slide 8
Let's Trace It Together
Settings: setpoint = 0.5 Kp = 0.5 base_effort = 0.3
sensor | error = 0.5 - sensor | correction = error * 0.5 | Left motor | Right motor | Which way?
0.5 | ? | ? | ? | ? | ?
0.2 | ? | ? | ? | ? | ?
0.8 | ? | ? | ? | ? | ?
0.1 | ? | ? | ? | ? | ?
0.6 | ? | ? | ? | ? | ?
Work through each row — calculate error, correction, and motor values.

## Slide 9
Answers Revealed
Settings: setpoint = 0.5 Kp = 0.5 base_effort = 0.3
sensor | error | correction | Left motor | Right motor | Which way?
0.5 | 0.0 | 0.0 | 0.30 | 0.30 | Straight
0.2 | +0.3 | +0.15 | 0.45 | 0.15 | Steer right (toward line)
0.8 | -0.3 | -0.15 | 0.15 | 0.45 | Steer left (away from line)
0.1 | +0.4 | +0.20 | 0.50 | 0.10 | Steer hard right
0.6 | -0.1 | -0.05 | 0.25 | 0.35 | Gentle steer left
Notice: bigger error → bigger correction → bigger difference between motors

## Slide 10
Two Sensors — Even Simpler
error = left_sensor - right_sensor # No setpoint needed!
Centered: Drifted left: Drifted right:
[L] LINE [R] [L] LINE [R] [L] LINE [R]
0.5 0.5 0.8 0.2 0.2 0.8
error = 0.0 error = +0.6 error = -0.6
"Go straight" "Steer left" "Steer right"
Why two sensors are better:
• One sensor: follows the EDGE of the line, can only see one side
• Two sensors: follows the CENTER of the line, can see BOTH sides
• No setpoint variable needed — the difference IS the error

## Slide 11
The Big Picture — Why This Matters
Proportional control is not just a robotics trick. It is everywhere:
System | Setpoint | Sensor | Correction
Shower temperature | Desired temp | Your skin | Turn the knob
Cruise control | Set speed | Speedometer | Throttle up/down
Line-following robot | 0.5 (edge) | Reflectance sensor | Steer left/right
Thermostat | 72°F | Thermometer | Heat on/off
The same pattern every time:
• 1. Measure where you are
• 2. Calculate how far off you are (error)
• 3. Respond proportionally
You now understand one of the most important ideas in engineering.

## Slide 12
Quick Check — Can You Answer These?
1. The sensor reads 0.3 and the setpoint is 0.5. What is the error?
Is it positive or negative? Which way should the robot steer?
2. Two students both have error = 0.3. Student A uses Kp = 0.2,
Student B uses Kp = 1.0. Whose robot steers harder?
Whose robot is more likely to oscillate?
3. Your robot is zigzagging wildly. Should you increase or decrease Kp?
4. Your robot slowly drifts off the line on curves.
Should you increase or decrease Kp?
5. Why can't we use straight() and turn() for line following?
What makes arcade() different?
Discuss with a partner, then we will go through them together.