## Slide 1
Module 2: Line Tracking
Lesson 9: Object Composition — LineTrack
Learning Objectives
Understand object composition (one class using another)
Build a LineTrack class that uses LineSensor
Create methods for line following and turning
Test classes with a simple main program
Agenda
Object composition concept (10 min)
Building LineTrack (20 min)
Testing and practice (15 min)

## Slide 2
From Messy Code to Clean Code
Lesson 7 (50+ lines, everything mixed together):
while True:
left = reflectance.get_left()
right = reflectance.get_right()
if left > 0.5 and right > 0.5:
drivetrain.stop()
drivetrain.turn(180)
time.sleep(0.3)
else:
error = left - right
# ... more code ...
What we want (3 lines!):
tracker = LineTrack()
tracker.track_until_cross()
tracker.turn_right()
Classes hide complexity behind simple names.

## Slide 3
What Is Object Composition?
Composition: One class contains and uses another class’s object.
Real-world analogy:
  A car HAS AN engine and HAS wheels
  The car doesn’t build the engine — it uses one
  The car delegates “go fast” to the engine
In our code:
  LineTrack HAS A LineSensor and HAS A DifferentialDrive
  LineTrack delegates “check sensor” to LineSensor

## Slide 4
LineTrack.__init__()
class LineTrack:
def __init__(self):
self.sensor = LineSensor() # Create a LineSensor
self.drivetrain = DifferentialDrive.get_default_differential_drive()
self.base_effort = 0.4
self.Kp = 0.5
self.sensor = LineSensor()
Creates a LineSensor object and stores it inside LineTrack.
Now LineTrack can call:
self.sensor.get_error()
self.sensor.is_at_cross()
self.sensor.is_off_line()

## Slide 5
track_until_cross()
def track_until_cross(self):
while not self.sensor.is_at_cross():
error = self.sensor.get_error()
left = self.base_effort - error * self.Kp
self.drivetrain.arcade(self.base_effort, -correction)
self.drivetrain.stop()
while not self.sensor.is_at_cross():
  Keep following while NOT at a cross
  When cross detected → loop exits → stop
Uses LineSensor methods for ALL sensor work.

## Slide 6
turn_right() and turn_left()
def turn_right(self):
# Drive forward to clear intersection
self.drivetrain.straight(5, 0.4)
# Turn right
self.drivetrain.turn(60, 0.4)
# Keep turning until line is found
while self.sensor.is_off_line():
Self.drivetrain.arcade(0, 0.4)
self.drivetrain.stop()
Three phases: Clear intersection → start turning → find line again
turn_left() is the same but with opposite motor directions.

## Slide 7
Using LineTrack in a Main Program
board = Board.get_default_board()
tracker = LineTrack()
board.wait_for_button()
tracker.track_until_cross()
tracker.turn_right()
tracker.track_until_cross()
The main program is clean and readable.
All complex sensor/motor code is hidden inside the classes.

## Slide 8
The Building Block Pattern
LineSensor DifferentialDrive
\ /
\ /
└───────┬───────┘
↓
LineTrack
↓
Main Program
Each layer builds on the layer below.
This is how professional software is built!

## Slide 9
Your Turn!
Exercise 1:
Build LineTrack and test each method
  track_until_cross() — does it follow and stop?
  turn_right() — does it turn and find the line?
Exercise 2 (Challenge):
Chain multiple maneuvers
for i in range(4):
tracker.track_until_cross()
tracker.turn_right()

## Slide 10
Connection to Final Project
You now have two reusable classes:
LineSensor — reads and interprets sensors
LineTrack — follows lines and handles intersections
Next (Lesson 10 — Final Project):
Follow circle → detect cross → reverse → repeat 4 times
Uses BOTH classes together
The capstone of Module 2!