## Slide 1
Module 1: Driving
Drawing Shapes
Learning Objectives
Use Repeat blocks to automate commands
Calculate turn angles for polygons
Draw squares, triangles, and other shapes
Understand repetition as a programming pattern
Agenda
Geometry review (10 min)
Repeat block introduction (5 min)
Guided: Draw a square (10 min)
Practice: Draw triangle & pentagon (20 min)

## Slide 2
Hook - How Does a Robot Draw?
Question: "How would the robot draw a square?"
Show: Video or animation of robot drawing square
Goes forward → turns → forward → turns → ... → back to start
Repeats same action 4 times
Key Insight: Computers excel at repetition

## Slide 3
Geometry Foundations
Regular Polygons:
Same length sides
Same angles at each corner
Close and return to start
Exterior Angle Formula:
360° ÷ Number of Sides = Turn Angle per Side
Why 360°? Full rotation = 360°
Examples:
Triangle (3 sides): 360 ÷ 3 = 120°
Square (4 sides): 360 ÷ 4 = 90°
Pentagon (5 sides): 360 ÷ 5 = 72°
Hexagon (6 sides): 360 ÷ 6 = 60°

## Slide 4
Introducing the Repeat Block
What is Repeat?
Runs code inside it N times
Reduces duplication
Makes program shorter and clearer
Blockly Appearance:
Repeat [4] times:
[Blocks inside]
Why Use It?
Draw square: 4 times, not 4 separate blocks
Easier to change (modify once, applies to all)
Match polygon structure (sides)

## Slide 5
The Square Program
Step-by-step:
Wait for button press
Repeat 4 times:
Straight(30) at 0.5 effort
Turn(90°) at 0.5 effort
Show: Blockly screenshot with complete program
Key Parameters:
4 repeats = 4 sides
30 cm = side length
90° = exterior angle (360÷4)
0.5 effort = speed

## Slide 6
Prediction & Testing
Before Running:
"Predict: What shape will the robot draw?"
Allow students to:
Trace path with finger
Sketch on paper
Discuss with partner
Then Run: Upload and observe
Discussion: Did it match your prediction? What differences?

## Slide 7
The Triangle Challenge
Goal: Draw a 3-sided shape
Calculation:
Number of sides: 3
Turn angle: 360 ÷ 3 = 120°
Distance: 25 cm (your choice)
Repeat block: Repeat 3 times
Code Structure:
Repeat 3 times:
Straight(25)
Turn(120°)

## Slide 8
The Pentagon Challenge
Goal: Draw a 5-sided shape
Calculation:
Number of sides: 5
Turn angle: 360 ÷ 5 = 72°
Distance: 20 cm (your choice)
Repeat block: Repeat 5 times
Interactive:
"What's the angle?" (Let students calculate)
"Show me on your hands" (Demonstrate with hand gestures)

## Slide 9
Angle Calculation Deep Dive
Why This Formula Works:
Robot makes same turn at each corner
4 corners × 90° = 360° (completes rotation)
6 corners × 60° = 360° (completes rotation)
Visual: Draw circle, show angle wedges
Test: "For an octagon, what's the angle?" (360÷8=45°)

## Slide 10
Shape Variations & Predictions
What If You Change Parameters?
Change | Effect | Shape
Repeat 4, Distance 50 | Bigger | Still square
Repeat 4, Distance 20 | Smaller | Still square
Repeat 6, Distance 20 | Different | Hexagon
Repeat 4, Angle 45 | Doesn't close | Not a square
Key: Sides determine shape; distance determines size

## Slide 11
Common Misconceptions
"The angle should be 90°, so my square has interior angle 90°"
Actually: 90° is EXTERIOR angle (turn angle)
Interior angle = 180° - 90° = 90° (different formula)
Both happen to be 90° for squares!
"More sides = bigger shape"
No! More sides = more corners, not larger perimeter
A 20cm triangle (perimeter 60cm) vs. 10cm hexagon (perimeter 60cm)

## Slide 12
Connection to Functions (Lesson 3)
Preview:
Today: Write three separate shape programs
Next lesson: Write ONE function that draws any shape
Use parameters: draw_polygon(sides, distance)
Teaser: "Imagine if you could draw ANY polygon with a single function call!"