## Slide 1
Module 4: Manhattan Navigation
Testing Without a Robot
Learning Objectives
Understand why testing without hardware is important
Write test programs that verify algorithm output
Compare computed paths against hand-calculated expected paths
Build confidence in code before deploying to hardware
Agenda
Why test without a robot? (5 min)
Writing test programs (10 min)
Systematic testing strategy (10 min)
Practice: Test your Manhattan class (20 min)

## Slide 2
Hook — Would You Fly an Untested Airplane?
Question: "Would a pilot fly a new airplane without testing it on the ground first?"
Of course not!
Test engines on the ground
Run simulations before flying
Check every system before takeoff
Same with robots:
Test the algorithm with print statements first
Verify the math is correct
THEN put it on the robot
Today's motto: "Test on screen before you test on the floor."

## Slide 3
The Separation of Concerns
Two separate problems:
Problem | Where it runs | What to test
Computing the path | Any computer | Does the path make sense?
Driving the path | On the robot | Does the robot follow correctly?
The Manhattan class computes paths — no motors needed!
manhattan = Manhattan((0, 0))
path = manhattan.compute_path((2, 3))
print(path) # Just prints — no robot required!
Benefit: Fix algorithm bugs BEFORE the robot drives into a wall.

## Slide 4
Writing a Test Program
Basic test structure:
manhattan = Manhattan((0, 0))
# Test 1: Basic forward path
path = manhattan.compute_path((2, 3))
print("Test 1 - (0,0) to (2,3):")
print(" Path:", path)
print(" Steps:", len(path) - 1)
print()
What to check:
Does the path start at the correct position?
Does the path end at the destination?
Is the number of steps correct (Manhattan distance)?
Does each step move exactly one row or one column?

## Slide 5
Expected vs. Actual
Compare what you expect with what you get:
# Expected path (from hand trace)
expected = [(0,0), (1,0), (2,0), (2,1), (2,2), (2,3)]
# Actual path (from your class)
manhattan = Manhattan((0, 0))
actual = manhattan.compute_path((2, 3))
# Compare
if actual == expected:
print("Test 1: PASS")
else:
print("Test 1: FAIL")
print(" Expected:", expected)
print(" Actual: ", actual)
This is the core of testing: Expected output vs. actual output.

## Slide 6
Systematic Test Cases
Test different scenarios:
def run_test(test_name, start, dest, expected):
manhattan = Manhattan(start)
actual = manhattan.compute_path(dest)
if actual == expected:
print(test_name, "- PASS")
else:
print(test_name, "- FAIL")
print(" Expected:", expected)
print(" Actual: ", actual)
Test cases to cover:
Test | Start | Dest | Tests
Forward right | (0,0) | (2,3) | Basic case
Backward left | (2,3) | (0,0) | Reverse direction
Same row | (1,0) | (1,3) | Column only
Same column | (0,2) | (3,2) | Row only
Same spot | (1,1) | (1,1) | No movement
One step | (0,0) | (0,1) | Minimal path

## Slide 7
Debugging with Print Statements
If a test fails, add print statements inside compute_path:
def compute_path(self, destination):
print("Computing path from", self.position, "to", destination)
path = [self.position]
current_row = self.position[0]
current_col = self.position[1]
# ... rest of code ...
print("Row step:", row_step)
print("Col step:", col_step)
while current_row != dest_row:
current_row = current_row + row_step
path.append((current_row, current_col))
print(" Added:", (current_row, current_col))
# ...
This lets you see exactly what's happening, step by step.
Remove print statements after debugging!

## Slide 8
Common Bugs and How to Find Them
Bug 1: Path missing the start position
Symptom: Path has 5 steps instead of 6
Fix: Make sure path = [self.position] (include start)
Bug 2: Path goes wrong direction
Symptom: (0,0) to (2,3) produces (0,0), (-1,0), (-2,0)...
Fix: Check row_step logic — should be +1 when dest > current
Bug 3: Infinite loop
Symptom: Program never finishes
Fix: If start == destination for that axis, the while loop should not execute
Bug 4: Off-by-one error
Symptom: Path goes one step too far or stops one step short
Fix: Check while condition — should be != not < or >

## Slide 9
Your Turn!
Activity:
Create a new file: test_manhattan.py
Copy your Manhattan class into it
Write at least 6 test cases using the table from Slide 6
Run the tests and verify all pass
If any fail, debug using print statements
Test template:
# Test 1: Basic forward path
manhattan = Manhattan((0, 0))
path = manhattan.compute_path((2, 3))
expected = [(0,0), (1,0), (2,0), (2,1), (2,2), (2,3)]
print("Test 1:", "PASS" if path == expected else "FAIL")
Checkpoints:
Do all 6 tests pass?
Did you test reverse directions?
Did you test edge cases (same row, same position)?

## Slide 10
Connection to Next Lesson
What you did today:
Learned why testing without hardware matters
Wrote systematic test programs
Verified your Manhattan class against expected outputs
Debugged any issues before touching the robot
Next lesson (Lesson 7):
Tackle the turning challenge — the robot needs to face the right direction
Learn about headings (North, South, East, West)
Figure out turn logic: "I'm facing North, I need to go East — turn right!"
Key insight: The algorithm is tested and working. Now we need to make the robot actually drive it!