## Slide 1
Module 4: Manhattan Navigation
Implementing the Navigator Class
Learning Objectives
Design the Navigator class with position and heading
Implement drive_path() to turn and drive through a path
Track and update heading as the robot moves
Integrate with DifferentialDrive for physical movement
Agenda
Class design overview (5 min)
Implementing helper methods (10 min)
Building drive_path() (15 min)
Testing on the robot (15 min)

## Slide 2
Hook — From Algorithm to Action
We have TWO pieces working:
Manhattan class computes the path (list of tuples)
Turning logic tells us what turns are needed
Missing piece: Something that actually DRIVES the robot!
path = [(0,0), (1,0), (2,0), (2,1), (2,2)]
# How does this become real robot movement?
Today: Build the Navigator class that turns and drives through any path.

## Slide 3
Navigator Class Design
What does the Navigator need?
Data (stored in __init__):
self.position — current (row, col) tuple
self.heading — current direction ("N", "S", "E", "W")
self.drivetrain — the DifferentialDrive object
Methods:
get_needed_direction(next_pos) — what direction to face
turn_to(direction) — turn the robot to face that direction
drive_one_step() — drive forward one intersection
drive_path(path) — drive the entire path

## Slide 4
The __init__ Method
Usage:
Note: The starting heading must match how you physically place the robot!
from XRPLib.differential_drive import DifferentialDrive
class Navigator:
def __init__(self, start, heading):
self.position = start
self.heading = heading
self.drivetrain = DifferentialDrive.get_default_differential_drive()
nav = Navigator((0, 0), "N")
print("Position:", nav.position) # (0, 0)
print("Heading:", nav.heading) # N

## Slide 5
get_needed_direction()
Determine direction from current position to next position:
Example:
def get_needed_direction(self, next_pos):
row_diff = next_pos[0] - self.position[0]
col_diff = next_pos[1] - self.position[1]
if row_diff == 1:
return "S"
elif row_diff == -1:
return "N"
elif col_diff == 1:
return "E"
elif col_diff == -1:
return "W"
nav = Navigator((0, 0), "N")
direction = nav.get_needed_direction((1, 0))
print(direction) # "S" — need to go south (row increases)

## Slide 6
turn_to()
Turn the robot to face the desired direction:
def turn_to(self, direction):
if self.heading == direction:
return # Already facing the right way
right_turns = {"N": "E", "E": "S", "S": "W", "W": "N"}
left_turns = {"N": "W", "W": "S", "S": "E", "E": "N"}
if right_turns[self.heading] == direction:
self.drivetrain.turn(90)
self.heading = direction
elif left_turns[self.heading] == direction:
self.drivetrain.turn(-90)
self.heading = direction
else:
# 180 degree turn
self.drivetrain.turn(180)
self.heading = direction
Key: Updates self.heading after turning!

## Slide 7
drive_path()
The main method — drive through every step in the path:
def drive_path(self, path):
for next_pos in path:
if next_pos == self.position:
continue # Skip the starting position
# 1. Figure out which way to face
direction = self.get_needed_direction(next_pos)
# 2. Turn if needed
self.turn_to(direction)
# 3. Drive forward one intersection
self.drivetrain.straight(30)
# 4. Update position
self.position = next_pos
print("Arrived at", self.position)
The loop: For each coordinate in the path, turn to face it, drive forward, update position.
Note: straight(30) assumes 30 cm between intersections — adjust for your grid!

## Slide 8
Putting It All Together
Complete test program:
from XRPLib.differential_drive import DifferentialDrive
from XRPLib.board import Board
class Manhattan:
# ... (from Lesson 5)
class Navigator:
# ... (from this lesson)
# Main program
board = Board.get_default_board()
manhattan = Manhattan((0, 0))
nav = Navigator((0, 0), "N")
board.wait_for_button()
# Compute and drive a path
destination = (2, 2)
path = manhattan.compute_path(destination)
print("Path:", path)
nav.drive_path(path)
print("Arrived at destination!")

## Slide 9
Your Turn!
Activity:
Implement the Navigator class with all four methods
Test with a simple path first: (0, 0) to (2, 0) — straight line, may need one turn
Then try: (0, 0) to (2, 2) — requires a direction change mid-path
Adjust the straight(30) distance to match your grid spacing
Debugging tips:
Print the heading and turn at each step
Start with a 2-step path before trying longer ones
Make sure the robot's physical starting heading matches "N" (or whichever you chose)
Checkpoints:
Does the robot turn correctly at each step?
Does it arrive at the right intersection?
Does the heading update properly?

## Slide 10
Connection to Next Lesson
What you did today:
Implemented the Navigator class with drive_path()
Integrated turning logic with physical robot movement
Tested on real paths
Next lesson (Lesson 9 — Final Project):
Integrate Manhattan + Navigator into a complete program
Navigate to a LIST of destinations (not just one)
Test with 4+ destinations on the grid
Key achievement: You now have TWO classes working together — one computes, one drives. That's separation of concerns in action!