## Slide 1
Module 2: Line Tracking
Lesson 2: Drive to the Edge and Stop
Learning Objectives
Write while loops in Python
Use comparison operators (<, >, ==)
Combine sensor reading with a while loop
Program the robot to drive until a condition is met
Agenda
while loops explained (10 min)
Guided practice: drive to edge (15 min)
Independent practice (20 min)

## Slide 2
The Problem
Last lesson:
We read sensor values, but the robot just sat still.
Today's goal:
Make the robot drive forward AND check the sensor continuously.
When it detects the line — stop!
Question:
"How do we repeat ‘drive and check’ without knowing how many times?"

## Slide 3
for Loop vs. while Loop
for loop (Module 1): Repeat a FIXED number of times
for i in range(4): # Always runs 4 times
drivetrain.straight(30)
drivetrain.turn(90)
while loop (NEW): Repeat UNTIL a condition changes
while left < 0.5: # Runs until left >= 0.5
drivetrain.set_effort(0.3, 0.3)
left = reflectance.get_left()
Key difference: for = fixed count. while = until something happens.

## Slide 4
while Loop Syntax
while condition:
# code that runs while condition is True
# code stops when condition becomes False
Rules:
Colon : after the condition
Indented body (same as for)
Condition is checked BEFORE each iteration
Loop exits when condition is False

## Slide 5
Comparison Operators
Operator | Meaning | Example | Result
`<` | Less than | 0.2 < 0.5 | True
`>` | Greater than | 0.8 > 0.5 | True
`==` | Equal to | 4 == 4 | True
`!=` | Not equal | 3 != 5 | True
`<=` | Less or equal | 5 <= 5 | True
`>=` | Greater or equal | 0.6 >= 0.5 | True
For sensors: left < 0.5 means “sensor is on white (below threshold)”

## Slide 6
Drive to the Edge
threshold = 0.5
board.wait_for_button()
left = reflectance.get_left()
while left < threshold:
drivetrain.set_effort(0.3, 0.3)
left = reflectance.get_left() # UPDATE!
drivetrain.stop()
print("Line detected!")
Step by step:
1. Read sensor before entering loop
2. While on white (below threshold) → drive forward
3. Update sensor reading EVERY iteration
4. When sensor hits line (above threshold) → loop exits → stop

## Slide 7
CRITICAL — Update Inside the Loop!
CORRECT:
while left < threshold:
drivetrain.set_effort(0.3, 0.3)
left = reflectance.get_left() # Updates!
WRONG:
while left < threshold:
drivetrain.set_effort(0.3, 0.3)
# left never changes → infinite loop!
Rule: Always update the variable you’re checking inside the while loop!

## Slide 8
set_effort vs. straight
drivetrain.straight(30)
Drives exactly 30 cm, then stops. BLOCKS until done.
drivetrain.set_effort(0.3, 0.3)
Sets motor power and returns IMMEDIATELY.
Why set_effort?
We need to check the sensor continuously.
straight() would drive the whole distance before we could check!

## Slide 9
Your Turn!
Exercise:
Place robot inside the taped circle.
Program it to:
  Wait for button press
  Drive forward
  Stop when it detects the line
Starter code provided — fill in the missing parts.
Checkpoints:
Robot drives forward?
Robot stops at the line?
Print shows sensor values?

## Slide 10
Connection to Next Lesson
Today:
Robot drives to the edge and STOPS.
Next lesson (Lesson 3):
Robot drives to the edge and TURNS AROUND!
  if/else statements — making decisions
  “Bounce driving” — robot bounces between edges of the circle
Preview:
if left > threshold:
drivetrain.turn(180) # Turn around!
else:
drivetrain.set_effort(0.3, 0.3) # Keep going