## Slide 1
Module 2: Line Tracking
Lesson 3: Bounce Driving
Learning Objectives
Write if/else statements in Python
Use while True for continuous robot behavior
Combine sensor checks with decision-making
Program the robot to bounce between circle edges
Agenda
if/else explained (10 min)
Bounce driving walkthrough (15 min)
Practice and experiment (20 min)

## Slide 2
From Stopping to Bouncing
Lesson 2:
Robot drives to edge → STOPS. Done.
Today:
Robot drives to edge → TURNS AROUND → drives again → repeat forever!
Like a ball bouncing off walls.

## Slide 3
if/else Syntax
Syntax:
if condition:
# runs when condition is True
else:
# runs when condition is False
Example:
temperature = 85
if temperature > 80:
print("It's hot!")
else:
print("It's comfortable.")
Only ONE block runs — never both.

## Slide 4
if/else for Robot Decisions
left = reflectance.get_left()
if left > threshold:
# ON the line — turn around!
drivetrain.stop()
drivetrain.turn(180)
else:
# OFF the line — keep driving
drivetrain.set_effort(0.3, 0.3)
When sensor > threshold:
On the line → stop and turn 180°
When sensor ≤ threshold:
Off the line → keep driving
The robot checks the sensor and decides what to do.

## Slide 5
while True — The Infinite Loop
while True:
# this code runs FOREVER
Why?
True is always True — the condition never becomes False.
For robots:
The robot should keep running until you turn it off.
Common in robotics — the robot continuously senses and acts.

## Slide 6
Complete Bounce Program
threshold = 0.5
board.wait_for_button()
while True:
left = reflectance.get_left()
if left > threshold:
drivetrain.stop()
print("Bounce!")
drivetrain.turn(180)
else:
drivetrain.set_effort(0.3, 0.3)
Flow:
Drive forward
Check sensor
On line? → stop, print, turn 180°
Not on line? → keep driving
Repeat forever

## Slide 7
Logical Operators
or — at least one must be True:
if left > 0.5 or right > 0.5:
print("At least one sensor on the line!")
and — both must be True:
if left > 0.5 and right > 0.5:
print("BOTH sensors on the line!")
not — reverses True/False:
if not (left > 0.5):
print("Left is NOT on the line")

## Slide 8
Using Both Sensors
while True:
left = reflectance.get_left()
right = reflectance.get_right()
if left > threshold or right > threshold:
drivetrain.stop()
drivetrain.turn(180)
else:
drivetrain.set_effort(0.3, 0.3)
Why both sensors?
If the robot approaches the line at an angle, only one sensor may detect it first.
Using or catches both cases.

## Slide 9
Your Turn!
Exercise 1:
Build the bounce driving program
  Robot bounces back and forth inside the circle
Exercise 2 (Challenge):
Use both sensors with or
Add a bounce counter
Observe:
What pattern does the robot follow?
Does it always bounce on the same line?

## Slide 10
Connection to Next Lesson
The problem:
The robot bounces back and forth on the SAME line. Boring!
Next lesson (Lesson 4):
Add randomness!
  import random
  random.randint() — generate random numbers
  Random turn angles → robot explores the whole circle
Preview:
angle = random.randint(90, 270)
drivetrain.turn(angle)