## Slide 1
Module 2: Line Tracking
Lesson 5: Proportional Control with One Sensor
Learning Objectives
Understand what a setpoint is and how to calculate error
Use set_effort() for continuous motor control
Build a proportional control loop for line following
Tune the Kp gain constant by observing behavior
Agenda
The problem with bounce driving (5 min)
set_effort() and continuous control (5 min)
Proportional controller step by step (20 min)
Follow the circle edge, tune Kp (20 min)

## Slide 2
What is Wrong with Bounce Driving?
Bounce driving (Lessons 3–4):
Drive straight → Hit line → Stop → Turn → Drive straight → Hit line → …
Problems:
  Jerky, not smooth
  Robot is NOT following the line — it is bouncing off it
  Cannot handle curves well
What we want:
  Robot smoothly follows the line
  Constant small adjustments, like steering a car
Question: "How can the robot steer while it is driving?"

## Slide 3
Blocking vs. Continuous Motor Control
Blocking calls (what we used before):
drivetrain.straight(30) # Drives 30 cm, then STOPS
drivetrain.turn(90) # Turns 90 degrees, then STOPS
Robot does one thing at a time
Cannot read sensors WHILE driving
Continuous control (new):
drivetrain.set_effort(0.3, 0.3) # Sets motors and KEEPS GOING
Sets motor power and returns immediately
Motors keep running until you change them
You can read sensors in between calls
Key difference: set_effort() does not block — the program keeps running.

## Slide 4
set_effort() Examples
Drive straight:
drivetrain.set_effort(0.3, 0.3) # Both motors equal
Turn right (left faster):
drivetrain.set_effort(0.4, 0.2) # Left faster than right
Turn left (right faster):
drivetrain.set_effort(0.2, 0.4) # Right faster than left
Values range from -1.0 (full reverse) to 1.0 (full forward) | set_effort(0.5, -0.5) = spin in place

## Slide 5
The Setpoint
From Lesson 1, you recorded sensor values:
  On white surface: ~0.1 to 0.3
  On the edge of the line: ~0.5
  On the black line: ~0.7 to 0.9
The setpoint is the target value we want to maintain.
setpoint = 0.5 # The edge of the line
Goal: Keep the sensor reading at the setpoint by making constant small steering adjustments.

## Slide 6
Calculating Error
Error = how far we are from where we want to be
error = setpoint - sensor_reading
Examples (setpoint = 0.5):
Where is the robot? | sensor_reading | error | Meaning
On the edge (perfect) | 0.5 | 0.0 | No correction needed
Drifted onto white | 0.2 | +0.3 | Steer toward line
Drifted onto black | 0.8 | −0.3 | Steer away from line
Positive error = robot is too far off the line (on white) — steer toward it
Negative error = robot is too far on the line (on black) — steer away
Zero error = perfect position — drive straight

## Slide 7
From Error to Correction
We multiply error by a gain constant Kp:
correction = error * Kp
Kp controls how aggressively the robot reacts. Example with Kp = 0.5:
error | correction = error × 0.5 | What happens
+0.3 | +0.15 | Gentle steer toward line
−0.3 | −0.15 | Gentle steer away from line
+0.4 | +0.20 | Stronger steer toward line
0.0 | 0.0 | Drive straight
Then apply correction to motors:
left_effort = base_effort + correction
right_effort = base_effort - correction

## Slide 8
The Complete Control Loop
setpoint = 0.5
Kp = 0.5
base_effort = 0.3
while True:
# 1. Read sensor
sensor_value = reflectance.get_left()
# 2. Calculate error
error = setpoint - sensor_value
# 3. Calculate correction
correction = error * Kp
# 4. Apply to motors
left_effort = base_effort + correction
right_effort = base_effort - correction
drivetrain.set_effort(left_effort, right_effort)
time.sleep(0.01)
The loop:
Read Sensor
↓
Calculate Error
↓
Calculate Correction
↓
Set Motors
↓ (back to top)
Runs hundreds of times per second!

## Slide 9
Tracing Through the Math
Scenario: Robot drifts onto white (sensor reads 0.2)
setpoint = 0.5
sensor_value = 0.2
error = 0.5 - 0.2 = 0.3
Kp = 0.5
correction = 0.3 * 0.5 = 0.15
base_effort = 0.3
left_effort = 0.3 + 0.15 = 0.45
right_effort = 0.3 - 0.15 = 0.15
Result: Left motor (0.45) faster than right (0.15) → robot steers right, back toward the line.
Scenario: Robot drifts onto black (sensor reads 0.8)
error = 0.5 - 0.8 = -0.3
correction = -0.3 * 0.5 = -0.15
left_effort = 0.3 + (-0.15) = 0.15
right_effort = 0.3 - (-0.15) = 0.45
Result: Right motor (0.45) faster → robot steers left, away from the line.

## Slide 10
What Does Kp Do?
Kp too low (0.1)
Robot drifts slowly away from line
Kp just right (0.5)
Robot smoothly follows the line
Kp too high (2.0)
Robot zigzags wildly across the line
Kp Value | Behavior
Too low (e.g., 0.1) | Robot reacts too slowly, drifts off the line
Just right (e.g., 0.5) | Robot follows smoothly with small adjustments
Too high (e.g., 2.0) | Robot overcorrects, oscillates wildly
Tuning Kp: Start at 0.5, lower if too wiggly, raise if too sluggish

## Slide 11
Exercise — Follow the Circle
Your task:
1. Type in the complete program
2. Place the robot on the edge of the taped circle
3. Press the button and observe
4. Tune Kp and base_effort for smooth tracking
Success:
Robot completes one full lap of the circle.
from XRPLib.differential_drive import DifferentialDrive
from XRPLib.reflectance import Reflectance
from XRPLib.board import Board
import time
drivetrain = DifferentialDrive.get_default_differential_drive()
reflectance = Reflectance.get_default_reflectance()
board = Board.get_default_board()
setpoint = 0.5
Kp = 0.5
base_effort = 0.3
board.wait_for_button()
while True:
sensor_value = reflectance.get_left()
error = setpoint - sensor_value
correction = error * Kp
drivetrain.set_effort(base_effort + correction,
base_effort - correction)
time.sleep(0.01)

## Slide 12
Connection to Lesson 6
What we accomplished today:
Smooth line following with ONE sensor using proportional control
Understood setpoint, error, Kp, and correction
Limitation of one sensor:
Only tracks one edge of the line
If the robot drifts too far off, it cannot tell which side it is on
Next lesson: Two-Sensor Line Following
Use BOTH left and right sensors
Error = left sensor − right sensor
Even smoother tracking, follows the CENTER of the line
Question: "Why might two sensors be better than one?"
error = reflectance.get_left() - reflectance.get_right()