## Slide 1
Module 2: Line Tracking
Lesson 7: Detecting Intersections
Learning Objectives
Detect when both sensors are on the line simultaneously
Use the and logical operator for combined conditions
Integrate intersection detection with line following
Program the robot to reverse direction at a cross
Agenda
What intersections look like to sensors (10 min)
Cross detection code (15 min)
Follow + detect + reverse (20 min)

## Slide 2
Adding the Cross
New physical setup:
A taped cross — a perpendicular line crossing the circle.
Question:
"When the robot reaches this cross while following the line, what will the sensors see?"
Answer:
BOTH sensors will be on the line at the same time!

## Slide 3
How Sensors See an Intersection
During normal line following:
One sensor on line, one off → different values
left ≈ 0.8, right ≈ 0.2 (or vice versa)
At an intersection (cross):
BOTH sensors on the line → both read high
left > 0.5 AND right > 0.5
This is our detection signal!

## Slide 4
The and Operator
if left > 0.5 and right > 0.5:
print("CROSS DETECTED!")
and truth table:
left > 0.5 | right > 0.5 | Result
True | True | True ← Cross!
True | False | False
False | True | False
False | False | False
Both must be True for and to be True.

## Slide 5
Line Following + Cross Detection
while True:
left = reflectance.get_left()
right = reflectance.get_right()
if left > threshold and right > threshold:
# Cross detected!
drivetrain.stop()
print("Cross!")
drivetrain.turn(180)
time.sleep(0.3)
else:
# Normal line following
error = left - right
left_effort = base_effort - error * Kp
right_effort = base_effort + error * Kp
drivetrain.set_effort(left_effort, right_effort)
Key design:
Check for cross FIRST, then do normal following.
Cross detected:
Stop, print, turn 180°, wait
Not a cross:
Two-sensor proportional following

## Slide 6
Why time.sleep() After Turning?
Without sleep:
Robot turns 180° → immediately re-reads sensors → still at the cross → turns again!
With sleep(0.3):
Robot turns 180° → pauses briefly → moves past the cross → resumes following
The sleep gives the robot time to move away from the intersection.

## Slide 7
Counting Crossings
cross_count = 0
while cross_count < 4:
left = reflectance.get_left()
right = reflectance.get_right()
if left > threshold and right > threshold:
cross_count = cross_count + 1
drivetrain.stop()
print("Cross #", cross_count)
drivetrain.turn(180)
time.sleep(0.3)
else:
# line following code...
print("Done! Crossed", cross_count, "times.")
This previews the final project!

## Slide 8
Alternative — Using a Function and a for Loop
Another way to count crossings:
Write a function that line-follows until it hits a cross, then use a for loop to call it 4 times.
def drive_to_cross():
"""Line-follow until a cross is detected."""
while True:
left = reflectance.get_left()
right = reflectance.get_right()
if left > threshold and right > threshold:
drivetrain.stop()
return # cross found — done
# normal line following
error = left - right
correction = error * Kp
drivetrain.arcade(base_effort, -correction)
for i in range(4):
drive_to_cross()
drivetrain.turn(180)
time.sleep(0.3)
Why this is nice:
The function does ONE job: drive until a cross
The for loop is simple and clear: do it 4 times
Easy to change: want 6 crosses? Just change range(4) to range(6)
Same result, different style!

## Slide 9
Your Turn!
Exercise 1:
Follow the circle and reverse at the cross
  Use two-sensor line following from Lesson 6
  Add cross detection with and
  Turn 180° when cross is detected
Exercise 2 (Challenge):
Count crossings and stop after 4
Test:
Does the robot reliably detect the cross?

## Slide 10
Connection to Next Lesson
What you’ve built so far (all as loose code):
Sensor reading, error calculation, cross detection
Proportional control, differential steering
All mixed together in one big program
Next (Lesson 8): Package sensor logic into a LineSensor class
get_error(), is_at_cross(), is_off_line()
First time writing a Python class!
Why? Organized code is easier to understand, test, and reuse.