## Slide 1
Module 2: Line Tracking
Lesson 6: Two-Sensor Line Following
Learning Objectives
Understand why two sensors are better than one
Calculate error using left and right sensors: error = left − right
Implement a two-sensor proportional control loop
Compare one-sensor and two-sensor line following
Agenda
Why one sensor is not enough (5 min)
Two-sensor error calculation (10 min)
Build and test two-sensor follower (15 min)
Compare one-sensor vs. two-sensor (20 min)

## Slide 2
The Limitation of One Sensor
One sensor (Lesson 5) follows the EDGE:
Problem scenarios:
  Robot drifts completely off the line to the right
  Sensor reads low (white)
  But is the line to the LEFT or to the RIGHT?
  One sensor cannot tell!
Solution: Use BOTH sensors — one on each side of the line.
"If you close one eye, can you still judge distances? What about with both eyes?"

## Slide 3
Two Sensors Straddle the Line
Position | Left Sensor | Right Sensor | Meaning
Centered | ~0.5 (medium) | ~0.5 (medium) | Both sensors at edge — drive straight
Drifted left | High (0.8+) | Low (0.2–) | Left on line, right on white — steer left
Drifted right | Low (0.2–) | High (0.8+) | Right on line, left on white — steer right
The difference between sensors tells us EVERYTHING:
  How far we drifted
  Which direction we drifted

## Slide 4
The Two-Sensor Error Formula
One sensor (Lesson 5):
error = setpoint - sensor_reading # Needs a setpoint!
Two sensors (this lesson):
error = reflectance.get_left() - reflectance.get_right() # No setpoint needed!
Robot Position | Left | Right | error = L − R | Meaning
Centered | 0.5 | 0.5 | 0.0 | Drive straight
Drifted left | 0.8 | 0.2 | +0.6 | Steer left to correct
Drifted right | 0.2 | 0.8 | −0.6 | Steer right to correct
Both on white | 0.1 | 0.1 | 0.0 | Off the line
Both on black | 0.9 | 0.9 | 0.0 | Intersection?

## Slide 5
Applying the Correction
Apply the correction with arcade:
correction = error * Kp
drivetrain.arcade(base_effort, -correction)
Why the signs?
If error is positive (drifted left, left sensor on line):
  Need to steer left to get back
  Slow down left motor (subtract), speed up right motor (add)
If error is negative (drifted right, right sensor on line):
  Need to steer right to get back
  Speed up left motor (subtracting a negative = adding), slow down right motor
Note: Signs are reversed from Lesson 5 because the error formula changed.

## Slide 6
Trace Through the Math
Scenario: Robot drifts left (left sensor on line)
left_sensor = 0.8
right_sensor = 0.2
error = 0.8 - 0.2 = 0.6
Kp = 0.5
base_effort = 0.3
correction = 0.6 * 0.5 = 0.3
arcade(0.3, -0.3) --> left = 0.0, right = 0.6
Left motor stops, right runs fast → robot turns left, back toward center.
Scenario: Robot drifts right (right sensor on line)
left_sensor = 0.2
right_sensor = 0.8
error = 0.2 - 0.8 = -0.6
correction = -0.6 * 0.5 = -0.3
arcade(0.3, 0.3) --> left = 0.6, right = 0.0
Right motor stops, left runs fast → robot turns right, back toward center.

## Slide 7
The Complete Two-Sensor Program
from XRPLib.differential_drive import DifferentialDrive
from XRPLib.reflectance import Reflectance
from XRPLib.board import Board
import time
drivetrain = DifferentialDrive.get_default_differential_drive()
reflectance = Reflectance.get_default_reflectance()
board = Board.get_default_board()
Kp = 0.5
base_effort = 0.3
while True:
# Read both sensors
left_sensor = reflectance.get_left()
right_sensor = reflectance.get_right()
# Calculate error
error = left_sensor - right_sensor
# Apply correction
correction = error * Kp
drivetrain.arcade(base_effort, -correction)

## Slide 8
One Sensor vs. Two Sensors
Feature | One Sensor (L5) | Two Sensors (L6)
What it follows | Edge of the line | Center of the line
Error formula | setpoint − sensor | left − right
Needs setpoint? | Yes (0.5) | No
Motor formula | base ± correction | base ∓ error×Kp
Smoothness | Good | Better
Recovery | Can only detect one side | Detects both sides

## Slide 9
Exploring Sensor Readings
Before running the control loop, explore the sensor values:
from XRPLib.reflectance import Reflectance
from XRPLib.board import Board
import time
reflectance = Reflectance.get_default_reflectance()
board = Board.get_default_board()
board.wait_for_button()
while True:
left = reflectance.get_left()
right = reflectance.get_right()
error = left - right
print(f"L={left:.2f} R={right:.2f} err={error:.2f}")
time.sleep(0.2)
Activity:
Slowly slide the robot across the line and watch how error changes.
Centered: error near 0
Left on line: error positive
Right on line: error negative

## Slide 10
Exercise — Two-Sensor Line Following
Your task:
1. Type in the two-sensor control program
2. Place the robot so the line runs between both sensors
3. Press button and observe the tracking
4. Add debug printing to see the values
Then compare:
5. Run your Lesson 5 (one-sensor) program on the same circle
6. Run the Lesson 6 (two-sensor) program on the same circle
Questions to answer:
Which version follows the line more smoothly?
Which version handles the curved parts better?
Which version can handle a higher base_effort without losing the line?

## Slide 11
A Curious Case — Both Sensors High
What happens when both sensors read high?
left_sensor = 0.9
right_sensor = 0.9
error = 0.9 - 0.9 = 0.0
Error is zero — the robot drives straight.
But what does it mean physically when both sensors see the line?
Answer: The robot might be at an INTERSECTION!
This is the key idea for Lesson 7: both sensors high = intersection detected.

## Slide 12
Connection to Lesson 7
What we accomplished today:
Smooth two-sensor line following
Error = left − right (no setpoint needed)
Smoother tracking than one sensor
Next lesson: Detecting Intersections
Add a taped cross to the circle
When both sensors read high: intersection detected
Robot stops, turns around, and continues in the opposite direction
"How can we tell the difference between 'centered on the line' and 'at an intersection'?"
if left_sensor > 0.5 and right_sensor > 0.5:
# We are at an intersection!
drivetrain.stop()
drivetrain.turn(180)