## Slide 1
Module 2: Line Tracking
Line-Tracking Functions
Learning Objectives
Build a second toolkit of functions that calls the Lesson 8 toolkit
Implement proportional line tracking inside a function
Implement turn functions that use sensor feedback
Test a multi-function program on the robot
Agenda
Two jobs, one robot (5 min)
Guided: Build the driving toolkit step by step (20 min)
Practice: Write and test your own toolkit (20 min)

## Slide 2
Hook -- Two Jobs, One Robot
Last lesson: a toolkit of sensor functions (reading)
But the robot doesn't just read sensors -- it also needs to drive
Should driving code go inside get_error()?
No -- keep sensor-reading and driving separate, same as Module 1 kept shape-drawing separate from setup.
The plan: a second toolkit -- driving functions -- that calls the sensor functions whenever it needs to know where the line is.

## Slide 3
The Relationship
Sensor toolkit (Lesson 8) Driving toolkit (Lesson 9)
get_left(), get_right() track_until_cross()
get_error() <---- turn_right()
is_at_cross(), is_off_line() turn_left()
Analogy: A car has an engine. The car doesn't rebuild the engine's parts inside itself -- it just uses the engine when it needs power.
Note for Classes track: this relationship is called object composition (LineTrack "has a" LineSensor). In the functions version, there's no "has" -- there's just "calls."

## Slide 4
Preview the Goal
track_until_cross()
turn_right()
track_until_cross()
Three lines to follow a line, detect an intersection, and turn.
Why keep them separate?
Sensor logic stays in Lesson 8 functions
Driving logic stays in Lesson 9 functions
The Lesson 8 toolkit could be reused in a program that never drives at all

## Slide 5
Step 1 -- The Driving Globals
from XRPLib.differential_drive import DifferentialDrive
drivetrain = DifferentialDrive.get_default_differential_drive()
BASE_EFFORT = 0.4
KP = 0.5
New globals, separate from reflectance/THRESHOLD from Lesson 8
Same file -- every function below (old and new) can see all four
BASE_EFFORT: baseline forward speed. KP: proportional control gain from Lesson 5

## Slide 6
Step 2 -- track_until_cross()
def track_until_cross():
while not is_at_cross():
error = get_error()
left = BASE_EFFORT - error * KP
right = BASE_EFFORT + error * KP
drivetrain.set_effort(left, right)
drivetrain.stop()
is_at_cross() and get_error() are called directly -- no prefix, because they're just names in the file's global scope
Proportional math is identical to Lesson 5, using global BASE_EFFORT/KP

## Slide 7
Step 3 -- Clearing the Intersection
When is_at_cross() becomes true, the sensors are over the intersection, but the turning center (rear axle) is still behind it.
def clear_intersection():
drivetrain.straight(8, 0.5)
Drives forward a fixed 8 cm -- an exact distance, not a timing guess
A small helper function, whose only job is to be called by the turn functions next
No timing-based movement anywhere in this course -- distance-based is consistent regardless of battery level

## Slide 8
Step 4-5 -- turn_right() and turn_left()
def turn_right():
clear_intersection()
drivetrain.set_effort(0.3, -0.3)
while is_off_line():
pass
drivetrain.stop()
def turn_left():
clear_intersection()
drivetrain.set_effort(-0.3, 0.3)
while is_off_line():
pass
drivetrain.stop()
Only difference between them: the motor efforts are swapped.

## Slide 9
Test the Complete Program
board = Board.get_default_board()
board.wait_for_button()
print("Following line...")
track_until_cross()
print("Cross detected! Turning right...")
turn_right()
print("Following line again...")
track_until_cross()
print("Done!")
Expected behavior: follows the line, stops at the cross, clears the intersection, turns right, follows again, stops.

## Slide 10
Demo Discussion & Connection to Lesson 10
How many lines of actual logic are in the test program? Just 3 function calls plus prints.
Where is all the sensor reading and motor control code? Organized into the two toolkits, out of the main program's way.
Coming up in Lesson 10: combine both toolkits into the Module 2 final project -- follow the circle, reverse direction 4 times.

## Slide 11
Optional Extension -- Refactor into a Class
For courses that also cover classes/objects. Skip if not covering classes.
class LineTrack:
def __init__(self):
self.sensor = LineSensor() # composition!
self.drivetrain = DifferentialDrive.get_default_differential_drive()
self.base_effort = 0.4
self.kp = 0.5
def track_until_cross(self):
while not self.sensor.is_at_cross():
error = self.sensor.get_error()
...
What changed: is_at_cross() becomes self.sensor.is_at_cross() -- delegating to the LineSensor object it contains, instead of calling a bare function.
This is object composition -- one class storing an instance of another class as an attribute (a "has-a" relationship).