## Slide 1
Module 2: Line Tracking
Module 2 Final Project
Learning Objectives
Integrate the sensor and driving toolkits into a complete program
Write a main program that follows the circle and reverses at the cross
Test, debug, and refine a working robot program
Present and reflect on your work
Agenda
Project overview & requirements (10 min)
Planning (15 min)
Implementation & testing (30 min)
Demo & reflection (15 min)

## Slide 2
Module 2 Journey
Your progress:
Lesson 1: Read sensors ✓
Lesson 2: while loops — drive to edge ✓
Lesson 3: if/else — bounce driving ✓
Lesson 4: import random — random turns ✓
Lesson 5: Proportional control ✓
Lesson 6: Two-sensor line following ✓
Lesson 7: Intersection detection ✓
Lesson 8: Sensor functions toolkit ✓
Lesson 9: Driving functions toolkit ✓
Today: Put it ALL together!

## Slide 3
Project Requirements
The robot must:
Follow the taped circle
Detect the cross intersection
Turn around (reverse direction)
Continue following
Repeat for 4 total reversals
Stop and print a completion message
Code must:
Use the sensor and driving toolkit functions
Include print statements showing progress
Be organized and commented

## Slide 4
Project Options
Option A: Standard (Recommended)
Follow → detect → reverse → repeat 4 times → stop
Use existing toolkit functions without modification
Option B: Enhanced
Option A plus: add turn_around() function, timing prints, LED feedback
Option C: Advanced
Option A plus: off-line recovery, variable speed, creative additions

## Slide 5
The Main Program
board = Board.get_default_board()
board.wait_for_button()
print("Starting!")
for i in range(4):
print("Leg", i + 1, "- Following...")
track_until_cross()
print("Cross! Reversing...")
turn_right()
turn_right()
print("Done! 4 reversals complete.")
The power of organized toolkits: The main program is just 10 lines!

## Slide 6
Testing Strategy
Test incrementally:
Test | What to Check
Test 1 | Does `track_until_cross()` follow to the cross?
Test 2 | Does the turn-around work?
Test 3 | Does 1 full reversal work?
Test 4 | Do all 4 reversals complete?
If something fails: Add print statements, check THRESHOLD, adjust parameters.

## Slide 7
Common Issues & Fixes
Problem | Fix
Robot doesn't detect cross | Adjust `THRESHOLD`, widen tape cross
Robot loses line after turn | Check `clear_intersection()`'s 8 cm against your robot
Robot goes wrong way after turn | Try `turn_left()` instead of `turn_right()`
Robot oscillates on the line | Reduce `KP` value
Robot is too slow/fast | Adjust `BASE_EFFORT`

## Slide 8
Rubric (50 points)
Category | Points
Code organization (toolkits correct) | 10
Line following works | 5
Cross detection works | 5
Reversal works | 5
Completes 4 reversals | 5
Testing evidence (prints) | 6
Debugging process | 4
Demo works | 4
Code explanation | 3
Reflection | 3
**Total** | **50**

## Slide 9
Build Time!
Steps:
Verify the sensor and driving toolkits work
Write main program
Test incrementally (1 reversal → 4 reversals)
Debug and tune
Prepare for demo
Ask for help if stuck — debugging is part of the process!

## Slide 10
Looking Ahead — Module 3
What you've built:
Reusable sensor and driving function toolkits
Skills: loops, conditionals, global variables, function composition
Module 3: Grid Driving
Use the driving toolkit on a taped GRID
track_until_cross() drives between intersections
turn_right() and turn_left() navigate the grid
Your Module 2 toolkits are the foundation for everything that follows!

## Slide 11
Optional Extension -- The Final Project with Classes
For courses that also cover classes/objects. Skip if not covering classes.
tracker = LineTrack()
board.wait_for_button()
for i in range(4):
tracker.track_until_cross()
tracker.turn_right()
tracker.turn_right()
Every call has a direct counterpart: tracker.track_until_cross() ↔ track_until_cross(), tracker.turn_right() ↔ turn_right(). Robot behavior is identical either way -- only the packaging differs.