## Slide 1
Module 3: Grid Driving
Driving Multiple Intersections
Learning Objectives
Explain why the robot must clear an intersection before continuing
Write code that drives past an intersection to the next one
Use a for loop to drive a specified number of intersections
Count intersections accurately
Agenda
The clearing problem (10 min)
Driving past an intersection (10 min)
For loops for counting (10 min)
Practice (15 min)

## Slide 2
Hook — The Stuck Robot
Demo: Robot drives to first intersection, stops.
Run track_until_cross() again...
Nothing happens! The robot doesn't move!
Why? The robot is still ON the cross. Both sensors are high. It thinks it's already at an intersection!
Question: "How do we tell the robot to keep going to the NEXT intersection?"

## Slide 3
The Clearing Problem
After track_until_cross(), the robot is AT the cross:
Line ──────+────── Line
|
[ROBOT] ← Sensors right on the cross!
|
Line
If we call track_until_cross() again:
Both sensors are already above threshold
is_at_cross() returns True immediately
The robot "detects" the intersection it's already on!
Solution: Drive forward briefly to move PAST the cross.

## Slide 4
Clearing the Intersection
The fix: Drive forward a short distance after detecting:
# Detect the intersection
track_until_cross()
# Clear the intersection (drive past it)
clear_intersection()
# Now we can detect the NEXT intersection
track_until_cross()
The clearing drive:
Low speed (0.3 effort) — don't go too fast
Short time (0.3 seconds) — just enough to move past
Adjust these values for your robot and grid spacing

## Slide 5
Driving Two Intersections
Complete program:
board.wait_for_button()
# Intersection 1
print("Driving to intersection 1...")
track_until_cross()
print("Reached intersection 1!")
# Clear
clear_intersection()
# Intersection 2
print("Driving to intersection 2...")
track_until_cross()
print("Reached intersection 2!")
This works! But what about 5 intersections? 10?

## Slide 6
Using a For Loop
A for loop makes it easy to drive any number of intersections:
intersections = 3
for i in range(intersections):
print("Driving to intersection", i + 1)
track_until_cross()
print("Reached intersection", i + 1)
# Clear (except after the last one!)
if i < intersections - 1:
clear_intersection()
Why skip clearing on the last intersection?
We want to STOP at the final intersection
That's where we'll turn or end the program

## Slide 7
Tracing the Loop
For intersections = 3:
i | Action | Clear?
0 | Drive to intersection 1 | Yes (0 < 2)
1 | Drive to intersection 2 | Yes (1 < 2)
2 | Drive to intersection 3 | No (2 < 2 is False)
Result: Robot drives through 3 intersections, stops at the 3rd.
Change to any number: Just change intersections = N

## Slide 8
Making It a Function
Wrap it in a reusable function:
Usage:
This function will be very useful in the final project!
def drive_intersections(count):
for i in range(count):
track_until_cross()
if i < count - 1:
clear_intersection()
drive_intersections(2) # Drive 2 intersections
drive_intersections(4) # Drive 4 intersections

## Slide 9
Your Turn!
Activity:
Write a program that drives exactly 2 intersections and stops
Modify it to drive 3 intersections
Create the drive_intersections(count) function
Test with different counts (1, 2, 3, 4)
Debugging: If the robot counts wrong:
Add print statements inside the loop
Check that clearing time is appropriate
Make sure you're not clearing after the last intersection
Checkpoints:
Does the robot stop at exactly the right intersection?
Does changing the count change the behavior?
Does your function work for any count?

## Slide 10
Connection to Next Lesson
What you did today:
Learned why clearing is necessary
Drove multiple intersections with a for loop
Created a reusable drive_intersections function
Next lesson (Lesson 3):
Add TURNS at intersections
Navigate L-shaped and more complex paths
Combine driving and turning in sequences
Preview: drive 2 intersections → turn right → drive 2 more = L-shape!