## Slide 1
Module 3: Grid Driving
Turning on the Grid
Learning Objectives
Sequence drive and turn operations on the grid
Use turn_right() and turn_left() at intersections
Navigate L-shaped paths on the grid
Plan a path on paper before writing code
Agenda
Turns at intersections (10 min)
The L-shape path (10 min)
Planning paths on paper (10 min)
Practice (15 min)

## Slide 2
Hook — Making Corners
So far: You can drive any number of intersections in a straight line.
New challenge: What if the destination isn't straight ahead?
Question: "How does the robot turn a corner on the grid?"
Answer: At an intersection, use turn_right() or turn_left() to switch to the perpendicular line!

## Slide 3
Turning at an Intersection
The robot must be AT an intersection to turn:
Before turn: After turn_right():
| |
────+──── ────+────
| |
[ROBOT] [ROBOT] →
What turn_right() does:
Drives forward briefly (clears the intersection)
Spins right
Stops when sensors find the perpendicular line
Key: After turning, the robot is already past the intersection — no extra clearing!

## Slide 4
The L-Shape Path
Drive 2 intersections forward, turn right, drive 2 more:
Visual:
Three lines of code, one L-shaped path!
drive_intersections(2)
turn_right()
drive_intersections(2)
Start → + → + ┐
↓
+
↓
+ ← End

## Slide 5
No Clearing After Turns
Important detail:
# After drive_intersections, robot is AT the intersection
drive_intersections(2)
# turn_right() handles clearing internally
turn_right()
# Go straight into next drive — no extra clearing!
drive_intersections(2)
Why? The turn method drives forward as part of the turn. The robot is already past the intersection.
Compare:
Between intersections in a straight line → must clear manually
After a turn → already cleared

## Slide 6
Planning Paths on Paper
Before coding, draw your path:
Step 1: Mark the grid on paper
Step 2: Draw the robot's path
Step 3: Write the sequence:
Drive N intersections
Turn left/right
Drive M intersections
Turn left/right
...
Example plan:
1. Drive 3 intersections forward
2. Turn left
3. Drive 2 intersections forward
4. Turn right
5. Drive 1 intersection forward

## Slide 7
More Path Examples
U-Turn:
Z-Shape:
Staircase:
drive_intersections(3)
turn_right()
drive_intersections(1)
turn_right()
drive_intersections(3)
drive_intersections(2)
turn_right()
drive_intersections(2)
turn_left()
drive_intersections(2)
for i in range(3):
drive_intersections(1)
turn_right()
drive_intersections(1)
turn_left()

## Slide 8
Common Mistakes
Mistake 1: Forgetting to be at intersection before turning
Mistake 2: Clearing after a turn
Mistake 3: Wrong turn direction
Plan on paper first!
Remember: turn_right() goes clockwise, turn_left() goes counterclockwise
# WRONG — robot is in the middle of a line
turn_right()
# CORRECT — drive to intersection first, then turn
track_until_cross()
turn_right()
# WRONG — double clearing causes skipped intersection
turn_right()
clear_intersection()

## Slide 9
Your Turn!
Activity:
Plan an L-shape on paper: 2 forward, right, 2 forward
Code it and test on the robot
Plan a different path (your choice) and code it
Challenge: Plan a path that returns to the starting position
Path ideas to try:
L-shape (2 forward, turn, 2 forward)
U-shape (3 forward, right, 1 right, right, 3 forward)
Staircase (repeat: 1 forward, turn, 1 forward, turn)
Checkpoints:
Does the robot follow your planned path?
Do the turns line up with the grid?
Can you predict where the robot will end up?

## Slide 10
Connection to Final Project
What you did today:
Combined driving and turning on the grid
Navigated L-shaped and custom paths
Planned paths on paper before coding
Next lesson (Lesson 4 — Final Project):
Drive a complete square on the grid
4 sides, 4 right turns, back to start
Use a for loop to repeat the pattern
The robot drives a closed path!
Preview: The square is just: for i in range(4): drive + turn