## Slide 1
Module 5: Dijkstra
Obstacle Detection with the Rangefinder
Learning Objectives
Read distance measurements from the XRP ultrasonic rangefinder
Determine whether an intersection is blocked using a distance threshold
Update a blocked-nodes list based on live sensor readings
Recompute a Dijkstra path after discovering a new obstacle
Agenda
What if the map is wrong? (5 min)
The ultrasonic rangefinder (10 min)
Reading distance at intersections (10 min)
Threshold logic: blocked or clear? (5 min)
Updating the blocked list and re-routing (10 min)
Practice exercise (10 min)

## Slide 2
Hook — What If the Robot Finds a Wall That Wasn't on the Map?
Question: "You gave the robot a list of blocked intersections before it started. But what if there's an obstacle the robot didn't know about?"
The problem:
So far, we hard-code the blocked list before the run
In the real world, obstacles appear unexpectedly
Construction, fallen objects, other robots — things change!
The solution: Give the robot a sensor so it can detect obstacles on its own.
Today: We'll use the XRP's ultrasonic rangefinder to detect obstacles at each intersection and reroute on the fly.

## Slide 3
The Ultrasonic Rangefinder
How it works: Sends out an ultrasonic pulse and measures how long the echo takes to return.
from XRPLib.rangefinder import Rangefinder
rangefinder = Rangefinder.get_default_rangefinder()
distance = rangefinder.distance() # returns distance in cm
Key facts:
Property | Value
Returns | Distance in centimeters (float)
Range | ~2 cm to ~400 cm
Update speed | Very fast — can read many times per second
Mounted on | Front of the XRP robot
What it detects: Any solid object in front of the robot — walls, boxes, other robots, your hand.

## Slide 4
Reading Distance at Intersections
Strategy: Check for obstacles BEFORE driving into the next intersection.
When to check:
After arriving at an intersection
Before deciding to drive to the next one
The robot is pointing in the direction it wants to go
What the readings mean:
# At each intersection, before moving forward:
distance = rangefinder.distance()
print(f"Distance ahead: {distance} cm")
distance > 30 cm → Path ahead is clear
distance < 15 cm → Something is blocking the path
15-30 cm → Gray zone — might be an obstacle approaching

## Slide 5
Threshold Logic — Is It Blocked?
We pick a threshold distance. If the reading is below the threshold, treat the intersection as blocked.
THRESHOLD = 15 # centimeters
distance = rangefinder.distance()
if distance < THRESHOLD:
print("Obstacle detected! Path is blocked.")
is_blocked = True
else:
print("Path is clear.")
is_blocked = False
Why 15 cm?
Close enough that the obstacle is definitely in the robot's path
Far enough that the robot has time to stop and reroute
You may need to adjust based on your grid spacing
Important: The threshold depends on how far apart your intersections are. Test and tune!

## Slide 6
Updating the Blocked List
When the robot detects an obstacle, add that intersection to the blocked list.
The blocked list grows as the robot explores:
Key idea: The robot builds its own map of obstacles through experience.
blocked_nodes = [] # starts empty — robot discovers obstacles
# At intersection (1, 2), robot checks ahead toward (1, 3):
distance = rangefinder.distance()
if distance < THRESHOLD:
next_intersection = (1, 3)
if next_intersection not in blocked_nodes:
blocked_nodes.append(next_intersection)
print(f"Added {next_intersection} to blocked list")
Run starts: blocked_nodes = []
After check 1: blocked_nodes = [(1, 3)]
After check 2: blocked_nodes = [(1, 3), (2, 1)]

## Slide 7
Which Intersection Is Ahead?
Before we can add to the blocked list, we need to know which intersection the rangefinder is pointed at.
NORTH = 0
EAST = 1
SOUTH = 2
WEST = 3
def get_next_intersection(current_pos, heading):
"""Return the intersection directly ahead of the robot."""
row, col = current_pos
if heading == NORTH:
return (row - 1, col)
elif heading == EAST:
return (row, col + 1)
elif heading == SOUTH:
return (row + 1, col)
elif heading == WEST:
return (row, col - 1)
We already have desired_heading() from Module 4 Lesson 8 doing the reverse of this. Here we just need the forward version: given position and heading, what's ahead?

## Slide 8
Re-routing After Detection
After discovering a new obstacle, rebuild the graph and recompute the path using the updated blocked list.
# At each intersection, before driving to the next one:
distance = rangefinder.distance()
if distance < OBSTACLE_THRESHOLD:
blocked_node = get_next_intersection(current_pos, heading)
if blocked_node not in blocked_list:
blocked_list.append(blocked_node)
print(f"Obstacle detected at {blocked_node}!")
print(f"Blocked list is now: {blocked_list}")
# Recompute the path with updated blocked list
graph = build_dijkstra_graph(rows, cols, blocked_list)
new_path = compute_dijkstra_path(current_pos, destination, graph)
print(f"New path: {new_path}")
The flow:
Robot arrives at intersection
Check rangefinder for obstacle ahead
If blocked: add to blocked list, rebuild the graph, recompute path from current position
If clear: continue on current path
Drive to next intersection
Repeat

## Slide 9
Your Turn!
Activity: Add Obstacle Detection to Your Navigation Program
Set up the rangefinder:
from XRPLib.rangefinder import Rangefinder
rangefinder = Rangefinder.get_default_rangefinder()
Before each move, read the distance and print it
Choose a threshold (start with 15 cm and adjust)
If an obstacle is detected:
Add the blocked intersection to your blocked list
Recompute the path using Dijkstra
Print the new path
Test by placing an object on the grid and watching the robot reroute
Checkpoints:
Can the robot read distance values from the rangefinder?
Does the robot correctly identify when an intersection is blocked?
Does the blocked list update when a new obstacle is found?
Does the robot recompute and follow a new path around the obstacle?

## Slide 10
Debugging Tips
Common issues and how to fix them:
Problem | Likely Cause | Fix
Distance always reads 0 | Rangefinder not connected | Check wiring and port
Robot detects "obstacles" that aren't there | Threshold too high | Lower the threshold value
Robot misses real obstacles | Threshold too low | Raise the threshold value
Robot gets stuck in a loop | Re-routing leads back to same blocked node | Make sure blocked list persists across recomputations
Path recomputation is wrong | Using old position as start | Use current intersection, not original start
Pro tip: Print the distance reading and blocked list at every intersection so you can see what the robot "sees."

## Slide 11
Connection to Next Lesson
What you did today:
Used the ultrasonic rangefinder to detect obstacles
Applied a threshold to decide if an intersection is blocked
Updated the blocked list dynamically during a run
Recomputed paths on the fly using Dijkstra
Next lesson (Lesson 8):
Make the robot remember obstacles across multiple runs
First run: discover obstacles and save them
Second run: start with knowledge from the first run
The robot gets smarter with experience!
Key insight: Today the robot discovers obstacles during a single run. Next lesson, it will carry that knowledge forward so it starts smarter each time.