## Slide 1
Module 1: Driving
Differential Drive & Motor Control
Learning Objectives
Understand how differential drive steering works
Control motors independently with set_effort
Compare high-level (Straight/Turn) vs. low-level (set_effort) control
Design complex movement patterns
Agenda
Motor basics review (5 min)
set_effort block introduction (5 min)
Guided: Arcade control patterns (8 min)
Challenge: Design figure-eight and spiral (15 min)

## Slide 2
Hook - How Does a Robot Turn?
Scenario: You have two motors
Straight: Both motors at same speed
Turn Right: Left motor faster than right
Question: "How much effort on each motor to make the robot turn 90°?"
This is differential drive steering!
Left motor: 50% effort →
Right motor: 50% effort →
Result: Robot goes straight
Left motor: 70% effort →
Right motor: 30% effort →
Result: Robot curves right

## Slide 3
Motor Control Architecture
Two-Motor Drive System:
Component | Function
Left Motor | Controls left wheel speed
Right motor | Controls right wheel speed
Combined effect | Steering (turn left/right)
Effort Range: 0.0 to 1.0
0.0 = Stopped
0.5 = Half speed
1.0 = Full speed
Negative Effort:
Reverses motor direction
-0.5 = Half speed backward

## Slide 4
The set_effort Block
What it does: Set motor speed directly (NOT distance-based)
Syntax:
Set left_motor effort to [0.5]
Set right_motor effort to [0.5]
Differences from Straight:
Straight: "Go forward 30cm" (robot does it)
set_effort: "Run at 50% speed" (keeps running until you stop it)
When to use set_effort:
✓ Continuous motion (don't know distance)
✓ Obstacle avoidance (change speed based on sensors)
✗ Precise distance (use Straight instead)

## Slide 5
Straight Line Movement
Balanced Effort:
Set left_motor effort to [0.5]
Set right_motor effort to [0.5]
Wait [2] seconds
Set left_motor effort to [0]
Set right_motor effort to [0]
Result:
Both motors same speed
Robot goes forward 2 seconds
Then stops
Key: Equal effort = straight line

## Slide 6
Turning Right
Asymmetric Effort:
Set left_motor effort to [0.7] ← Left faster
Set right_motor effort to [0.3] ← Right slower
Wait [1] second
Set left_motor effort to [0]
Set right_motor effort to [0]
What Happens:
Left wheel travels faster
Robot pivots around right wheel
Results in clockwise turn
Effort Difference:
Just slightly unequal: Gentle curve
Very unequal: Sharp turn

## Slide 7
Turning Radius & Control
Gentle Turn (subtle effort difference):
Sharp Turn (large effort difference):
Spin in Place (opposite efforts):
Relationship:
Effort difference → Steering sharpness
Motor speed → Forward/backward speed
Left: 0.6, Right: 0.4 → Wide curve
Left: 0.8, Right: 0.2 → Tight curve
Left: 0.5, Right: -0.5 → Rotates without moving forward

## Slide 8
Arcade Control Pattern
Simpler abstraction for differential drive:
Parameters:
forward_speed: -1 to 1 (negative = backward)
turn_rate: -0.5 to 0.5 (negative = turn left)
Examples:
def arcade_drive(forward_speed, turn_rate):
left_effort = forward_speed + turn_rate
right_effort = forward_speed - turn_rate
arcade_drive(0.5, 0): ✓ Straight forward at 50%
arcade_drive(0.5, 0.3): ✓ Forward + turn right
arcade_drive(0, 0.5): ✓ Spin right in place
arcade_drive(-0.5, 0.3): ✓ Backward while turning right

## Slide 9
Complex Movement Patterns
Figure-Eight Pattern:
Spiral Pattern:
Zigzag Pattern:
Turn right (effort 0.7, 0.3) for 1.5 seconds
Turn left (effort 0.3, 0.7) for 1.5 seconds
Repeat to create infinity loop
Start: 0.5, 0.5 (straight)
Gradually: Left motor increases, right decreases
Create outward spiral
Straight (0.5, 0.5) for 1 second
Turn left (0.3, 0.7) for 0.5 second
Turn right (0.7, 0.3) for 0.5 second
Repeat

## Slide 10
set_effort vs. Straight Comparison
Movement Comparison:
Task | Use set_effort | Use Straight
Go forward exactly 50cm | ✗ | ✓
Continuous movement | ✓ | ✗
Obstacle avoidance | ✓ | ✗
Precise path | ✗ | ✓
Speed control only | ✓ | -
Complex patterns | ✓ | ✗
Key Difference:
set_effort: You manage duration (with Wait blocks)
Straight: Robot manages distance (you just specify it)

## Slide 11
Safety with Continuous Motion
Always Include:
Set effort (start motor)
Wait (duration)
Set effort to 0 (stop motor!)
DANGER - No Wait Block:
DANGER - No Stop Block:
CORRECT:
Set left_motor to 0.5
Set right_motor to 0.5
→ Robot NEVER STOPS (infinite forward)
→ Crashes into wall
Set left_motor to 0.5 ← Goes forward
... later ...
Set left_motor to 0.7 ← Changes speed, keeps going
→ No explicit stop → keeps moving
Set left_motor to 0.5
Wait 2 seconds
Set left_motor to 0 ← STOP!

## Slide 12
Connection to Python (Lessons 9-10)
Preview:
Today: Blockly set_effort blocks for motor control
Lesson 9: Python loops to automate Wait/set_effort cycles
Lesson 10: Python functions for arcade_drive and patterns
Python Version (sneak peek):
left_motor = 0.5
right_motor = 0.5
wait(2)
left_motor = 0
right_motor = 0
Teaser: "Python makes repeated motor patterns much cleaner!"