## Slide 1
Module 2: Line Tracking
The Reflectance Sensor
Learning Objectives
Explain how reflectance sensors detect light vs. dark surfaces
Read sensor values using the Reflectance class
Record calibration data for your specific robot and surface
Choose a threshold value for line detection
Agenda
How sensors work (10 min)
Reading sensor values (15 min)
Calibration exercise (20 min)

## Slide 2
Hook — How Does a Robot "See"?
Question: "You can see the black line. How could a robot tell the difference?"
Discussion: Robots don't have eyes — they use sensors that measure physical properties.
Today: We'll learn to read the XRP's reflectance sensors — the robot's way of "seeing" the line.

## Slide 3
How Reflectance Sensors Work
The sensor has two parts:
Infrared LED — shines light downward
Light detector — measures how much bounces back
White surface: Reflects most light → low value (close to 0.0)
Black surface: Absorbs most light → high value (close to 1.0)
Analogy: Flashlight on a mirror vs. a black t-shirt
Show: Photo of XRP underside with sensors highlighted

## Slide 4
Sensor Value Range
Values range from 0.0 to 1.0:
Position | Left Sensor | Right Sensor
On white surface | ~0.1 – 0.3 | ~0.1 – 0.3
On line edge | ~0.4 – 0.6 | ~0.4 – 0.6
On black line | ~0.7 – 0.9 | ~0.7 – 0.9
Key idea: The transition from white to black is GRADUAL, not sudden.
The XRP has TWO sensors — left and right — each reads independently.

## Slide 5
Reading Sensors in Python
Import and setup:
Read values:
Key point: get_left() and get_right() return a number between 0.0 and 1.0.
from XRPLib.reflectance import Reflectance
from XRPLib.board import Board
reflectance = Reflectance.get_default_reflectance()
board = Board.get_default_board()
board.wait_for_button()
left = reflectance.get_left()
right = reflectance.get_right()
print("Left:", left, "Right:", right)

## Slide 6
Continuous Reading
Read many times in a loop:
import time
board.wait_for_button()
for i in range(50):
left = reflectance.get_left()
right = reflectance.get_right()
print("Left:", left, " Right:", right)
time.sleep(0.1)
Why? See how values change as you move the robot across the line.
time.sleep(0.1) — pause 0.1 seconds so readings aren't too fast to read.

## Slide 7
What Is a Threshold?
Threshold: A cutoff value to decide "on line" vs. "off line"
Example:
Off line readings: 0.1, 0.2, 0.15, 0.25
On line readings: 0.75, 0.8, 0.85, 0.9
Threshold = 0.5 (halfway between)
Rule: If sensor > threshold → on the line. If sensor < threshold → off the line.
Important: The threshold depends on YOUR surface and tape. Calibrate!

## Slide 8
Calibration Exercise
Your task:
Place robot on WHITE surface → record sensor values
Place robot on BLACK line → record sensor values
Place robot on EDGE of line → record sensor values
Calculate your threshold (halfway between off-line and on-line averages)
Why calibrate? Different surfaces, tape colors, and lighting conditions give different values.
Save your threshold! You'll use it for the rest of Module 2.

## Slide 9
Your Turn!
Activity:
Create sensor_test.py
Write the continuous reading program
Collect calibration data for 3 positions
Record in your worksheet
Determine your threshold value
Checkpoints:
Can you read sensor values?
Do white and black give different numbers?
Did you find a good threshold?

## Slide 10
Connection to Next Lesson
What you did today:
Learned how reflectance sensors work
Read sensor values in Python
Calibrated your sensors and chose a threshold
Next lesson (Lesson 2):
Use a while loop to keep the robot driving
Stop when the sensor detects the line
First time the robot uses sensors to control its behavior!
Save your calibration data — you'll need it!